## Slide 1: Neural network-based imitation of model predictive control for power converters
Aitor Teran, Cristina Roche, Pere Izquierdo

## Slide 2: CONTENT
FS-MPC
ANN IMITATOR METHOD
RESULTS
CONCLUSION

## Slide 3: MODEL
Notes: The classic. Traditional 2-level inverter with LC output filter.
Discretized state-space model.

## Slide 4: FS-MPC
Optimal decision
Algorithm that uses the model of the system to predict the control action that minimizes error.
Notes: FS-MPC stands for finite-set model predictive control.
Model predictive because it makes use of a model of the system to compare predictions to references, finite-set because there’s a limited number of control outputs.
Explain the figure.
Disadvantage: computational requirements.

## Slide 5: PROPOSED SOLUTION
Low computational burden.
Ability to imitate different controllers.
Inputs
Outputs
Notes: The proposed solution is to use a neural-network-based imitator.
A neural network is computationally cheap universal approximator.
Neural network basics: each neuron computes previous values times weight vector and adds a bias value, then going through a nonlinear activation function.

## Slide 6: DATA ACQUISITION
2 million training data points
1 million random validation and test data points
Notes: Explain the control scheme. Inputs: reference voltage, output voltage, inductor current, load current, previous system state.
Network trained using TensorFlow in Python using 2 million grid-generated data points within the operating range of the lab setup.
Validation and testing of the neural network performed on 1 million random data points inside the same bounds.

## Slide 7: TRAINING THE NETWORK
Finding the optimal network configuration.
1 hidden layer with 15 neurons.
98% test accuracy
Notes: Finding network configuration: activation functions, cost function, optimization algorithm. Non-convexity of training a neural network.
Adding several layers does not significantly improve the performance of the network.
For a single layer, error and THD values are compared to obtain the optimal number of neurons.

## Slide 8: RESULTS
Why is the same figure shown twice?
ANN
MPC
Notes: This slide shows how good the ANNs are at approximating MPC.
Very similar THD and switching frequencies.
1-step MPC takes 10 us, 2-step takes 13 us. ANNs always take 11 us.

## Slide 9: RESULTS
Imitator transient response
Notes: Fast and accurate load transient response.
Current spike because of switching device.

## Slide 10: RESULTS
Imitator robustness
Ability to extrapolate to untrained data
Robust to voltage reference changes
Notes: Surprisingly, the imitators are robust to changes in reference voltage amplitude and frequency, even though they were not trained for it.

## Slide 11: CONCLUSION
The imitation method removes the computational limitations of FS-MPC, while maintaining its performance.
ANNs show great potential for application in the field of power electronics.
In principle, the method could be used for any control scheme.
Notes: Surprisingly, the imitators are robust to changes in reference voltage amplitude and frequency, even though they were not trained for it.

## Slide 12: THANK YOU
THANK YOU