## Slide 1: Neural network-based imitation of model predictive control for power converters
Aitor Teran, Cristina Roche, Pere Izquierdo

## Slide 2: CONTENT
INTRODUCTION
PROBLEM ANALYSIS
FS-MPC
NEURAL NETWORKS
ANN IMITATOR METHOD
RESULTS
DISCUSSION
CONCLUSION
FUTURE WORK

## Slide 3: INTRODUCTION
Short execution time
Pattern recognition
Modelling of nonlinear systems
Potential of Artificial Neural Networks (ANN):
Control of power converters?
Notes: Artificial neural networks have been a fundamental part of many research breakthroughs in recent years due to their ability to execute complex structures in short processing times, to find patterns from data for modelling relationships for which no mathematical description exists or is not accurate, i.e. to approximate any continuous function. This high potential is aimed to be applied to power converters

## Slide 4: PROBLEM ANALYSIS
Artificial neural networks
Finite set model predictive control
Imitator controller
Resistive load
Simple inverter topology
Sampling time 20 µs
Control of power converters?
Limitations
Notes: The main goal is to obtain an artificial neural network that is able to imitate the finite set model predictive control algorithm for inverter control purposes, achieving similar performance while reducing its computational requirements.
The inverter to be controlled is a three-phase six switch inverter connected to a resistive load, therefore the objective of this project is to prove whether neural networks have potencial to be applied to power converters field, characterized by a short control signals period. The sampling time is fixed to 20 micro seconds because mpc to be executed needs that period and this is needed for experimental comparison purposes

## Slide 5: MODEL
Notes: The model of the plant basically consists in the filter. The second order low pass filter is formed by an inductor in series and a capacitor in parallel, i.e a LC circuit. The inverter dynamics are considered to be ideal. This filter is used to attenuate the amplitude of the harmonics to get a smooth sinusoidal fundamental wave.
(dead time is not modelled because inverter is considered to be ideal)

## Slide 6: MODEL
State space
Notes: LTI system, state space model representation, being u the control signals, ir.e the switching vectors and the current through the load. The states are the voltage through the load or capacitor and the ouput current of the inverter.
The goal of the state space model is to be used as a simulation for finding the rate of change of the state variables. Given the input signal and the previous states values, the model can be used to predict the system behaviour in the next sampling instant.

## Slide 7: FS-MPC
Optimal decision
Algorithm that uses the model of the system to predict the control action that minimizes error.
Notes: -FS-MPC stands for finite-set model predictive control.
-Model predictive because it makes use of a model of the system to compare predictions to references, finite-set because there’s a limited number of control outputs, which are the 8 possible switching combinations. Through the states prediction it compares them with the reference and choose the proper control decision that tracks the reference the best.
-Explain the figure: Predictions are obtained for each possible control action through the use of the state space model of the system. Then, the performance of each control action is compared by calculating the cost function for each of them. The chosen control action will be applied in the next sampling instance. (it gives the switching command, so no modulation technique is needed).
-MPC can use different number of steps predictions to take the decision. In the figure only for one step ahead prediction is shown, therefore the model has to be run 8 times. In case the decision can be made taking into account 2 steps ahead behaviour, for each of these again 8 possible switching states should be considered, therefore 8^2 combinations, which results in running the model 64 times, which requires high execution time. And the number of calculations to be performed online increases exponentially.

## Slide 8: FS-MPC
Notes: For one step ahead prediction the diagram shows the steps followed by MPC, both zero vectors for simplification are taking as only one control action, so we only have 7 possible control outputs.
-First, at the beginning of every sampling period ,i,.e. k, we get the new measurements x(tk) in abc reference frame. This is transformed to alfa-beta reference frame through vector projection.
-Through the state space model the values of the states in the next sampling time can be estimated (x^(tk+1)). This estimation is the output estimation that the setup is gonna give in the next sampling time with the already decided control action. This is called delay compensation.
-the model is run again but now in a loop for each of the 7 possible switching states and the estimated values. These gives 7 possible outputs for tk+2.
-the cost function of each is computed.
-with the 7 cost functions, the minimum one gives the switching state chosen to be applied at tk+1
X(tk):
Three pahses of:
(States)
Filter currents iL (measured)
Capactitor voltages vc (measured)
(inputs)
Load currents (measured)
Applied voltage to the filter (the previously output of the state space model by the optimal decision)

## Slide 9
FS-MPC – Cost function
Flexible decision
Any state or variable can be included
Decision based on linear or non-linear behaviour
Basic cost function: reference tracking
Notes: The goal of the cost function is to proper compute a value that represent how good that control decision (switching state) is.
FS MPC takes decision based on a cost function, or function that penalise not desired behaviours.
This makes MPC flexible and broadens the control possibilities, because any state or variable of the system can be included in the decision logic and can decide based on linear or non linear behaviour also.
Basic one: Euclidean distance between the desired and the obtained voltages.

## Slide 10: FS-MPC – Cost function
Secondary objectives: derivative dynamics
Notes: Secondary objetives can be several, but based on literature, we chose a derivatives of the load voltage term
Again the Euclidean distance between the dereivative of the voltage reference and the derivative of the load voltage is penalized.
This results in very improved performance of the mpc for one step horizon. Because the switching state chosen could be the best one for the sampling instant but have large derivative at that point, and therefore lead to a worse value in the next sampling instant.

## Slide 11: FS-MPC – Cost function
Weighting factor
Notes: Terms in the cost function are added through a weighting factor.
Trade-off decision
Its tested and in terms of thd phase voltage the best value is 1.

## Slide 12: FS-MPC- Advantages and drawbacks
Flexible control actions decision through the cost function
-Accurate transients
-Multiple and non-linear based decisions
Sampling time: trade-off decision FS-MPC execution time < Sampling time
A short sampling time
- improves the performance
- limits the number of steps ahead horizon
- limits the complexity of the possible converter
SOLUTION: to run MPC offline and train an ANN with the data
Notes: Advantages: Flexible control actions through the cost function, which allows to hace accurate transients and to make control actions decisions based on multiple objectives and non linear dynamics.
Disadvantages: the sampling time decision is a trade-off decision, it has to be longer than the mpc execution time. Therefore, a short sampling time is needed to improve the performance because the frequency of the control actions is increased and therefore the precision of the output. However, it limits the number of steps ahead horizon and the possible complexity of the converter topology.
The solution to this disadvantage is to run mpc offline, to not to have the sampling time requirement and train a ANN with this data, and then control with the ANN because its execution time is lower.